## Slide 1
Levels of Building Fire Risk Modeling
Workflow and Generic Modeling Framework for Community Fire Risk Analysis
Chupei Lin

## Slide 2
EXISTING FIRE-RISK MODELS · EXAMPLE 1 OF 4
Event Trees
Probabilistic decomposition of an initiating event into success/failure branches
KEY IDEA
An event tree examines the success and failure of systems following an initiating event (e.g., ignition).
Each branch is assigned a probability;
the leaves give the likelihood of every scenario
With the probability of each scenario, simulation tools are used to analyze the consequences.
Strengths
Transparent decision logic
Quantifies low-probability tails
Limitation
Static
Assumes branch independence and fixed probabilities
Fig. Typical event tree for a fire event in a building. Adapted from Tan et al. (2019).
2 / 14

## Slide 3
EXISTING FIRE-RISK MODELS · EXAMPLE 2 OF 4
Bayesian Networks
Directed acyclic graph of variables and conditional dependencies
KEY IDEA
Nodes represent random variables;
arcs encode causal relations between variables.
Computes posterior probabilities of outcomes given evidence.
Probabilistic, not deterministic.
Strengths
Handles partial evidence
Captures correlations between variables
Updates as new data arrives
Limitation
Requires informed conditional-probability tables.
Fig. Bayesian network for human fatalities in a fire. Adapted from Hanea and Ale (2009).
3 / 14

## Slide 4
EXISTING FIRE-RISK MODELS · EXAMPLE 3 OF 4
Traditional Fire-Frequency Models
Volume / floor-area + activation-risk classification
Generalized Barrois model
Tilander & Keski-Rahkonen, 2003
Ignition frequency:
A is the floor area; c₁, c₂, r, s are coefficients, which are determined experimentally from observations for different building categories.
Building categories
Residential buildings
Industrial buildings & warehouses
All other buildings
Matrisk Fire Probability Model (top-down)
Annual fire probability:
α, β, γ are determined by activation-risk class; V is the building volume.
Activation-risk classification (VKG)
No risk | Small | Medium | High
Room without electrical installations, without intended fire and without activating hazards | Retail, Shopping centers, Parking, Library, Hospital rooms | School classrooms, Restaurants (commercial), Industry buildings | Residential use, Hotel rooms, Kitchen use
4 / 14
Matrisk BSV report, 2025
Classified based on the purpose code of the Association of Cantonal Building Insurance

## Slide 5
EXISTING FIRE-RISK MODELS · EXAMPLE 4 OF 4
Spatial Regression Models
OLS extended with three forms of spatial dependence
THREE SPATIAL REGRESSORS
1
Spatially lagged dependent variable
y depends on neighbors' y (ρWy term)
2
Spatially lagged explanatory variables
neighbors' X influence local y (WXγ term)
3
Spatially lagged error term
residuals correlated with neighbors (λWu term)
Fig. Ordinary Linear Regression hierarchy with spatial dependence. Adapted from Bispo et al. (2023).
5 / 14

## Slide 6
INTRODUCTION
The Problem and Research Gap
Fires remain a substantial risk to life, property, and urban infrastructure — risk-reduction decisions operate at two scales
BUILDING-LEVEL
Consequence analysis
SCALE
Single building
METHODS
Event/fault trees, Bayesian networks
INPUTS
Building & occupant-behavior factors
KEY WORKS
Matellini et al. (2013) · Hanea & Ale (2009) · Tan et al. (T-H-O) (2021)
COMMUNITY-LEVEL
Occurrence prediction
SCALE
Urban area / community / census tracts
METHODS
Spatial regression, machine learning
INPUTS
Socio-demographic predictors (income, density, housing age)
KEY WORKS
Buffington et al. (2021) · Bispo et al. (2023) · Hao et al. (2023)
Research Gap · A generic model connecting occurrence / ignition and consequence for building-level fire-risk analysis.
6 / 14

## Slide 7
Multi-Scale Fire Risk for Community Risk Management
Forward propagation generates risk; backward selection refines models and data
Forward propagation
Backward selection
DATA
MODEL
FIRE-RISK
ASSESSMENT
DECISION
Training procedure
Prediction procedure
Inputs (training set)
fire events + features
Building-level data
(building area, occupancy)
Community-level statistical data
(socio-demographic factors)
Training
fit · validate · select
Building-level generic fire-risk model
Fire events
(training output)
Building fire-risk
assessment
Community fire risk
(aggregated)
Building-level decisions
(risk-reduction measures)
Community-level decisions
(risk-reduction measures)
7 / 14
Aggregation
Building-level
Community-level
VOI
Sensitivity analysis

## Slide 8
COMMUNITY-LEVEL INPUTS
Critical Factors for Fire Occurrence
Predictors and effects identified in the empirical literature
HUMAN-RELATED
The number of occupants
More occupants → more ignition sources, greater exposure.
Population density is the most critical predictor (Buffington et al. 2021, Bispo et al. 2023, Ma et al. 2023)
Income
Low-income communities cannot afford detectors, maintenance, or fire-safe heating.
Higher income → lower fire incidence (Duncanson et al. 2002, Buffington et al. 2023).
Education-level
Lower education → reduced risk awareness → higher fire frequency
(Corcoran et al. 2007, Hu et al. 2019, Anderson-Bell et al. 2021).
BUILDING-RELATED
Building volume / area
Building usage
Activation-risk class (VKG): residential, hotel, retail, industrial, etc.
Age / condition / degradation
Poor housing quality creates structural vulnerabilities:
Deteriorated wiring, failing heaters, substandard materials → higher ignition rates.
Captured via pre-1950 stock (Buffington), degraded density (Bispo), post-1980 ratio (Ma).
Bispo et al. (2023) represent this factor through degraded building density; Buffington et al. (2021) through pre-1950 housing stock; and Ma et al. (2025) through the ratio of buildings constructed after 1980.
Time effect
Cold winters drive seasonal peaks consistently across U.S. regions (Ma et al. 2025).
Spatial effect
Spatial dependence demonstrated at census-tract level in Portugal (Bispo et al. 2023).
8 / 14
Effects
Tradition model
Proxy
To occupants' behaviors

## Slide 9
FIRE-RISK MODEL — OCCURRENCE / IGNITION
Level 1 · Traditional (Volume-based) Models
Fire rate λ as a function of building volume / floor area and building (activation-risk) type
LEVEL
1
POISSON FRAMEWORK
Annual number of fire incidents:
NF = annual fire-incident count in a building
λ = fire rate (modelled at three levels)
LEVEL 1 · TRADITIONAL
Building volume / floor area as proxy for occupant population
V building volume
type building usage type / activation-risk class (VKG)
f( · ) empirical fit (Barrois / Matrisk)
Limitation Ignores socio-demographic and temporal predictors. Volume alone is a coarse proxy for the true ignition drivers.
9 / 14
Level 1: Volume
Level 2: Socio-demographic factors + Linear additive
Level 3: Nonlinear intercorrelated

## Slide 10
FIRE-RISK MODEL — OCCURRENCE / IGNITION
Level 2 · Linear-Additive with Socio-Demographic Predictors
Volume + linear contributions from input variables, hierarchical across spatial scales
LEVEL
2
MODEL FORMULATION
Add a generalized linear-additive part:
Assumption: Input variables are independent
X socio-demographic variables
coefficient vector
Spatial-temporal extension (time effect):
Seasonal / temporal heterogeneity captured via .
HIERARCHICAL BAYESIAN
Individual building → Community → City → Country
Country level
City level
Community level
10 / 14
Assumption:
within the same community, is the same at the building level

## Slide 11
FIRE-RISK MODEL — OCCURRENCE / IGNITION
Level 3 · Nonlinear with Variable Correlations
Capturing interactions and complex relationships among input variables
LEVEL
3
VARIANT A · VOLUME INDEPENDENT
Building volume kept independent;
nonlinear function for the remaining input variables.
f(V) traditional volume-based contribution
g(X) nonlinear function of socio-demographic / building factors
Captures complex correlations among inputs while preserving the well-understood role of building volume.
VARIANT B · FULLY GENERALIZED
All inputs, including building volume, enter a single nonlinear function.
g( · ) fully nonlinear (e.g. GAM, neural network)
Most flexible: captures interactions and correlations among all input variables.
Trade-off: less interpretability, higher data requirements.
11 / 14

## Slide 12
GENERIC MODELING FRAMEWORK
Fire-Induced Fatalities
Hazard · Exposure · Vulnerability — performance-based fire-safety design for consequence analysis
Performance-based fire-safety design: timelines, damage states, and occupant states for fatality estimation.
12 / 14
HAZARD
Building-level data
Community-level statistical data
Building-level generic model
Fire ignition
Damage state
EXPOSURE
Occupants
VULNERABILITY
ASET
Occupant
behavior
Building
characteristics
RSET
Fire fighting
Probability of fatalities
Major

## Slide 13
VULNERABILITY DEEP-DIVE
ASET / RSET — Inputs and Sub-Timeline Uncertainty
Each sub-time is itself uncertain; ASET and RSET combine to determine fatality probability
ASET — Available Safe Egress Time
RSET — Required Safe Egress Time
Time from ignition
Ignition (t = 0)
Detection
Sensors react
Alarm
Notification
Pre-movement
Decide, prepare
Movement
Walk to exit
RSET
Last occupant out
ASET
Untenability
Fatality occurs when RSET > ASET.
Definition
Time from ignition until conditions become untenable for occupants.
Drivers
Fire-growth curve (slow / medium / fast / ultra-fast), compartment geometry, ventilation, and the chosen untenability criterion.
Inputs
Fire-growth rate
Peak heat-release rate (HRR)
Ventilation conditions
Compartment volume
Definition
Detection + alarm + pre-movement (reaction) + movement time required for occupants to evacuate.
Drivers
Pre-movement varies from under a minute (alert workers) to many minutes (sleeping occupants, mobility-limited, or those attempting to fight the fire).
Movement depends on geometry, exit width, density, and walking speed.
Inputs
Occupant population (age, mobility, familiarity)
Pre-movement time distribution
Exit availability and geometry
Alarm reliability

## Slide 14
QUANTIFYING UNCERTAINTY
Sources of Uncertainty
Model and inputs for the model; ASET and RSET each contribute consequence-side uncertainty
Model
M
Parameters uncertainty
uncertainty in fitted coefficients (β, σ²) and prior choices
Model-structure uncertainty
wrong functional form, omitted variables, residual errors
Input variables
X
Statistical-level inputs
income, education, housing age reported at tract / census level — not available per individual building
Consequence analysis · ASET
A
Ignition location & initial fuel load
Heat-release rate · Fire-growth rate
Flashover probability and timing
Ventilation conditions (doors/windows open or closed?)
Suppression activation time & effectiveness
Zone-model uncertainty
CFD model
Consequence analysis · RSET
R
Each sub-time is a random variable
detection · alarm · pre-movement · movement
Population heterogeneity
age, mobility, familiarity vary across the occupant pool
Behavioral uncertainty
decisions under stress, mis-perceptions, panic, group dynamics
14 / 14

## Slide 15
CLOSING
Conclusion
A generic probabilistic model connecting occurrence and consequence for building-level fire-risk analysis
Goal · A generic probabilistic model connecting occurrence and consequence for building-level fire-risk analysis.
Why probabilistic
Fire-risk analysis exposes uncertainty explicitly; instead of a conservative deterministic estimate, we report what we don’t know and make better decision-making under risk with the distribution of possible outcomes.
Why building-level
Building-level models capture fine-grained building and occupant detail.
Why Bayesian networks
A graphical model encodes the conditional dependence structure among key factors; expert knowledge (and/or data) supplies the conditional probability tables; the DAG makes the inference logic intuitive.
Then what
Use the model to support decision-makers and policy-makers: reduce community-level fire risk and identify the most influential factors for each individual building.
15 / 17

## Slide 16
DECISION SPACE
Decisions
Risk-reduction and urban-planning decisions identified in the literature
RISK REDUCTION
Single building
Intervention
Matellini et al. (2018) · Hao et al. (2023)
Performance-based structural fire design
Hasofer et al. (2007) · Chu & Sun (2008) · Gernay et al. (2016) · Zhang et al. (2017)
URBAN PLANNING
Portfolio / community
Resource allocation
Buffington et al. (2021) · Wu et al. (2026) · Song et al. (2017) · Hossain (2023)
Fire-station location planning
Bispo et al. (2023) · Cui et al. (2024) · Lee et al. (2025)
Insurance risk stratification
De Sanctis & Fisher (2015) · Du et al. (2025)
Open questions
- Which decisions matter most for community fire-risk management?
- Given an estimate of fatality risk in a building, what decisions does it support, and for whom?
- In fire risk analysis/modeling, where does uncertainty matter most?
16 / 17

## Slide 17
INPUTS
Data
Critical factors identified from literature and additional sources needed
FOR THE MODEL
Identified critical factors
Building information
Building volume
Building type
Building age / condition / degradation
Occupant information
Number of occupants
Income status
Education level
WANTED
Wanted data
Fire event reports
Building-level incident records.
Fire occurrence statistics
Census-tract / municipality fire-related data with socio-demographic predictors.
17 / 17